## Slide 1
Performance analysis framework for base station placement using IEEE 802.11
Group study presentation
Rustam Khakov
Kirill Kukartsev
Zufar Makhmutov
18.03.2020
Notes: Kirill
1

## Slide 2
Problem Description

## Slide 3
Increasing coverage and capacity
with UAV equipped with base stations[1]
Motivation
Mobile users’ demand increasing
  Higher speed, lower latency
  More data and services
Tendency to be located closely to users
  2G: Macro-cells
  3G - 4G: Micro-cells
  5G: Pico-cells
  Idea: Unmanned Aerial Vehicle with
  Base Stations (UAV-BS)
Problems:
  How to design a placement algorithm?
  How to evaluate correctness of the algorithm?
  How to coordinate the elements of mobile
  communication system infrastructure?

## Slide 4
A General Use-Case for Possible Solution
A Generalized Use-Case for a Placement Algorithm Experimental Framework

## Slide 5
Architecture Description

## Slide 6
Abstract System Design
Abstract Design for component interaction for the given possible problem solution

## Slide 7
Framework Architecture Description
GPS_Tracker
GPS_Android
GPS_Frontend
Three main component of framework: a phone (GPS_Android), user interface (GPS_Frontend), data processing (GPS_Tracker)
Notes: Rustam
1

## Slide 8
Android Component
Measure:
  GNSS location
  RSS of Wifi connection
  Connection speed
GPS_Android installed on an Android SmartPhone
Requirements:
- Android above 4.0
- GNSS connection
- Access to Wifi

## Slide 9
Activities:
- Send measurement result to given server
- Measure data periodicaly on
background with given timeout

## Slide 10
Android Application Architecture

## Slide 11
GPS_Frontend
User Interface to interact with GPS_Tracker
Single Page Application (SPA)
Based on web technologies
Main features
  Model-View-ViewModel design pattern
  Parallel execution, asynchronous calls
  Reactivity
  Extensibility
Representation of MVVM design pattern elements
Notes: Now we will discuss the most visual part of our framework – GPS_Frontend.
This is a web based user interface to access link measurement data from mobile phones. Also it provides functions to run optimization tasks and analyze result of them.
User Interface built with Model-View-ViewModel design pattern shown on the slide.
Here we have three components:
View – objects shown to user, like tables, div, columns, images.
ViewModel – component that defines operation on data representing in Model. May separate partly data contract with Model component.
Model – storage for user data. There are specified getters and setters for data objects. All data sink communication (to external DB, local DB, different transformation) defined here.
1

## Slide 12
Technologies for GPS_Frontend
Components
  VueJS – a Javascript framework for SPA
  Vuex – data storage library
  Vuerouter – URL path router
  Plotly – plotting library
  Bootstrap – web design library
Alternatives
  Angular – by Google, functional, but monolithic
  React – by Facebook, flexible, but not easy-to-go
  VueJS – by community, flexible, lightweight, but not so functional
The most popular libraries logos for modern web projects: Angular, React, VueJS
Notes: We can point out 5 technologies in GPS_Frontend
- VueJS - a Javascript web framework, the skeleton of application
- Vuex - a unite data storage to share between components
- Vuerouter - URL path routing
- Plotly - to plot figures
- Bootstrap - an open-source toolkip, to make UI good looking.
- Angular has rich functionality, but too complex for that task.
- React is more fexible, but requires more time to get working in.
- Vue.js is a simple framework with an excellent documentation but has a lack of components in the default conguration. It requires additional libraries and components to design required functions.
1

## Slide 13
GPS_Frontend-Visualization
Location data on given
timeframe
Timeframe,
update
frequency
configuration
Database
statistics
Layout of the UI implemented by GPS_Frontend. The user access UI in a web-browser
Notes: This is a view where you can show and analyze measurements received from the phone.
Control Menu
Database Statistics
Graphical View
  Signal Changes
  Signal Heatmap
  Client Measurement Technology
  Link throughput Measurements
1

## Slide 14
GPS_Frontend-Estimation
UEs positions for optimization task
Available task results
Choose parameters for new task
Notes: This is another view of GPS_Frontend where you work with placement opltimication algorithms
Control Menu
Estimation Menu
Available Estimation Results
1

## Slide 15
GPS_Tracker
Functions
  Serve HTTP REST inquires
  Process incoming messages from GPS_Android
  Dispatch optimization tasks
Key features
  Worker design pattern
  Python programming language
Key technologies
  Lightweight Flask library for HTTP server
  Celery task scheduling library
  MongoDB NoSQL database
  RabbitMQ message queue
Notes: Then we are going to discuss our backend part called GPS_Tracker.
This is set of backend programs intended to serve user requests, process incoming messages from GPS_Androi and perform optimization tasks.
The GPS Tracker is implemented in Python language. This is a dynamic interpreting language. That is known the performance is not so perfect compared to
static compiled languages, but it has higher changeability property.
1

## Slide 16
GPS_Tracker Subsystems
Component Diagram for GPS_Tracker subsystems
Notes: This s component diagram of GPS_Tracker
I would like to point out two subsystem
Processing Subsystem
  FTP
  MQTT (with middleware) or DataBackend
Storage Subsystem
  Interface
  MongoDB
1

## Slide 17
Master-Worker Interaction Diagram
A typical interaction diagram for Worker design pattern
Notes: Speaking about Worker design pattern, it provides useful architecture:
- Linear performance scaling
Load balancing
Fast feedback to users
1

## Slide 18
System Component Deployment
Two main cases
  Bare-metal installation
  Containerized deployment
Key features
  Interaction via network
  Components can be separated geographically
  Virtual machines and containers runtime
Reason for virtual machines
  Independence of hardware
  Virtual hardware specification control
  Single way of installation – just bring an VM image
Reason for containers
  Provide ready-to-use program environment
  Concept isolation – explicit specification of dependencies
  Resource isolation – cgroups and namespaces
  Convenient development and deployment
Abstraction Layers for Hardware and Operation system virtualization
Notes: Another unique think is the deployment process of our framework.
We provide flexible way to install and run the system – you can use real hardware that gives you the maximum performance, or you can use containerized environment.
We provide already prepared virtual machine image, where software components are running in containers.
There are pros and cons when your add so many run-time abstraction, but nevertheless, advantages outweighs possible problems.
1

## Slide 19
Deployment Diagram In Containers
Notes: Finally, you can see deployment plan using containers.
We have three entry points:
Tcp 80/443 – to access web interface.
Tcp 5000 – to access REST API
Tcp 21 – to access FTP to perform link throughput measurements
Internally, Docker (a set of platform to run OS-level virtualization – container) set-up overlay network for containers and take care of correct routing between them. Therefore, as long as your containers are running in the same machine or cluster, you don’t have to worry about network connectivity.
1

## Slide 20
Experiment Description

## Slide 21
Experiment Description
Communication between components during the experiment
Notes: Zufar
1

## Slide 22
Network Diagram of Experiment
A network scheme of experiment
Notes: Zufar
1

## Slide 23
Sub-Optimal Case
Notes: Zufar
1

## Slide 24
Uniform Case
Notes: Zufar
1

## Slide 25
Near-Uniform Case
Notes: Zufar
1

## Slide 26
Experiment 1
Goals:
  initial try
  as many UEs as possible
  collect errors
Conditions:
  6 UEs, 1 CnC, 2 APs
  cloudy sky, snow on the ground, -1 .. +1 °
Decisions:
  resolve the second AP failure reasons
  add logs to UEs

## Slide 27
Experiment 2
Goals:
  check new speed estimation algorithm
  discover UEs errors using logs
  better track overall changes in front-end
Conditions:
  3 UEs, 1 CnC, 1 APs
  clear sky, no snow, strong winds
Decisions:
  add logging to APs as well
  implement direct HTTP requests

## Slide 28
Experiment 3
Goals:
  compare HTTP requests instead of MQTT
  completely refactored app
Conditions:
  3 UEs, 1 CnC, 1 APs
  indoor (TU Ilmenau Mensa building)
Decisions:
  one more scaled-up experiment
  run placement algorithm

## Slide 32
Experiment 4
Goals:
  three cases (sub-optimal, uniform, near-optimal)
  run placement algorithm
Conditions:
  6 UEs, 1 CnC, 2 APs
  light rain
Decisions:
  analyze collected data
  figure out why 2 UEs positions were wrong

## Slide 36
Optimized positions for UAV-BS
Logical map for the original position and suggested optimized position. Coordinates by “clustering” (K-Means) position optimization algorithms are highly biased.
Satellite map with original and suggested positions for UAV-BS layout
Notes: Zufar
1

## Slide 37
Final result
Are the initial aims fulfilled?
 | Aspect | Result
Developed system | Functional properties | Works as expected, but had to alter architecture
Stability / Performance / Usability | Link may suffer collisions
Optimization algorithm | Provided positions | Calculated correctly
Stability / Performance / Usability | Extra data and/or other algo for higher accuracy
Result of 4 performed experiments
Notes: Zufar
1

## Slide 38
Overview
Notes: Zufar
1

## Slide 39
Questions?
Thank for your attention!

## Slide 40
References
A. Syromiatnikov and D. Weyns, "A Journey through the Land of Model-View-Design Patterns," 2014 IEEE/IFIP Conference on Software Architecture, Sydney, NSW, 2014, pp. 21-30. doi: 10.1109/WICSA.2014.13
Ropero, Juan & Tamura, Gabriel. (2017). Characterizing the Impact of Context-Variables in Software Performance Factors: a Domain-Specific Design Patterns Perspective. 10.13140/RG.2.2.13879.42408.
Prateek Sharma, Lucas Chaufournier, Prashant Shenoy, and Y. C. Tay. 2016. Containers and Virtual Machines at Scale: A Comparative Study. In Proceedings of the 17th International Middleware Conference (Middleware ’16). Association for Computing Machinery, New York, NY, USA, Article 1, 1–13.
Zhao, Nan & Yu, F. & Fan, Lisheng & Chen, Yunfei & Li, Jie & Tang, Jie & Nallanathan, Arumugam. (2019). Caching UAV-Enabled Small-Cell Networks. IEEE Vehicular Technology Magazine.
Notes: 1

## Slide 41
Appendix. Android Class Diagram

## Slide 42
Appendix: UI And Backend Interaction
New optimization task registration
Notes: Now I would like to discuss one of the most interesting features implemented in GPS_Tracker.
Optimization tasks can take long to complete, and if we start optimization task in the same thread that serving a user request, it will hand the user until the task is done. To make UI responsible and interactive, we use Python Celery library to implement Worker pattern when performing an optimization task.
1

## Slide 43
Appendix. Deployment Diagram of Framework
Dockerized infrastructure
Unified interface
Configuration in .config or OS env
A deployment case in container runtime.
Notes: Kirill
1

## Slide 44
Appendix. Resolved problems
Problem | Group | Resolved way
Can’t install app via apk | Android | Install using Android Studio
Data doesn’t come to CnC | Wi-Fi | Check AP
Silent crash of app | Android | Added logging to file in phone
Error related to MQTT | Software | Replace MQTT with HTTP
Hard to describe software architecture | Report | Refactor code to follow MVVM pattern
Table describes significant moments of workflow
Notes: Zufar
1

## Slide 45
Appendix. Experiment 1/4
Measured signal link speed for uplink and downlink. Mostly metrics are degraded, cannot truly rely on them.
Notes: Zufar
<номер>

## Slide 46
Appendix. Experiment 2/4
Overall detected coordinates changes during the experiment. Clearly shown that GPS has measurement error.
Notes: Zufar
<номер>

## Slide 47
Appendix. Experiment 3/4
The heatmap of quality of WI-FI signal by GPS coordinates.
Notes: Zufar
<номер>

## Slide 48
Appendix. Experiment 4/4
Notes: Zufar
<номер>